## Slide 1
HeartPrint: Passive Heart Sounds Authentication Exploiting In-Ear Microphones
Yetong Cao∗, Chao Cai†, Fan Li∗, Zhe Chen‡, Jun Luo§
*Beijing Institute of Technology, China
†Huazhong University of Science and Technology, China
‡China-Singapore International Joint Research Institute, China §Nanyang Technological University, Singapore
INFOCOM 2023

## Slide 2: Background
ANC earphones with in-ear microphones (IEMs) are booming.
Earphone authentication methods hamper the normal function of earphones or cause inconvenience to users.
Speaker occupation
Tooth occlusion
Speaker occupation & jaw movement
IEMs
Acoustic Sensing

## Slide 3: Existing Works
Heart-based biometrics has emerged as a popular authentication method.
Secure
Unique
Measurable
Nonvolitional
Can we reusing the IEMs of ANC earphones to capture the unique and fine-grained heart sounds (PCGs) as biometrics to enable pure passive user authentication?
Liveness
Existing approaches are limited.
Rely on special hardware
Require user efforts

## Slide 4: Basic Idea
Heart properties
Geometric shape
Volume
Moving dynamics
Bone-conduction patterns
Bone structures
Bone densities
Bone-tissue ratios
Body asymmetry patterns
Left and right path are different

## Slide 5: Basic Idea

## Slide 6: Basic Idea
Wide availability
Ubiquitous deployability
Transparent operations

## Slide 7: Feasibility Study
Left
Ear
Right
Ear
Conclusion
Different users exhibit clear distinctions in bone-conducted PCGs.
Individual users also exhibit discernible body asymmetry patterns.
User 1
User 2
User 3
User 4

## Slide 8: Feasibility Study
Left
Ear
Right
Ear
Conclusion
The same users hold consistent patterns across different sessions.
User 4
Session 1
User 4
Session 2
User 4
Session 3

## Slide 9: Feasibility Study
t-SNE projection of CWT for four users across ten sessions
The binaural bone-conducted PCGs contain sufficient biometrics that is unique across users and remains consistent over time.

## Slide 10: HeartPrint
Challenge 3: How to address biometrics shift over time?
Challenge 2: How to extract unique and secure biometric information?
Challenge 1: How to remove interference without impairing the general usage of earphones?

## Slide 11: Interference Elimination
Interference filtering
Interference eliminating based on modified Non-negative Matrix Factorization
160Hz low-pass filter
Signal decomposition
Body sounds
Background audio
STFT
Traditional NMF:
Traditional NMF can not handle the wide spectrum of interference.

## Slide 12: Interference Elimination
Interference filtering
Interference eliminating based on modified Non-negative Matrix Factorization
160Hz low-pass filter
Signal decomposition
Body sounds
Background audio
STFT
Modified NMF:

## Slide 13: Interference Elimination
Interference filtering
Interference eliminating based on modified Non-negative Matrix Factorization
160Hz low-pass filter
Signal decomposition：
Body sounds
Background audio
STFT
Modified NMF:
+

## Slide 14: Interference Elimination
Interference filtering
Interference eliminating based on modified Non-negative Matrix Factorization
160Hz low-pass filter
Signal decomposition
Body sounds
Background audio
Bone-conducted PCGs reconstruction
  Identify bone-conducted PCGs based on cosine distance
  Inverse STFT
Interference elimination

## Slide 15: Representation Extraction
- Observation: PCGs hold distinctions in the frequency domain due to heart dynamics.
- Feature: 16 Mel frequency cepstral coefficients (MFCCs) features of each ear (162 in total).
Sound wave propagation model
Decayed sound pressure
Sound source
Decay property
Propagation distance
Heart motion feature
- Observation: Bone-conducted PCGs contain unique information about the conduction properties of bone and tissue.
- Feature: 16 linear prediction coefficients (LPCs) features of each ear (162 in total).
Body conduction feature

## Slide 16: Representation Extraction
- Observation: PCGs from two ears exhibit different degrees of enhancement or attenuation at different frequencies and time frames.
- Feature: (1) Divide the bond-conducted PCGs of each ear into 32 parts according to frequency range between 0-160Hz (each part has a bandwidth of 5Hz).
(2) Compute the Euclidean distances (EDs) between the left and right ears’ in-ear sounds of each part (321 in total).
Body asymmetry feature
Final biometrics
LPCs (left ear)
MFCCs (left ear)
LPCs (right ear)
MFCCs (right ear)
EDs

## Slide 17: Authentication Decision
CNN-based deep learning framework
-Structure:
  - Three convolution blocks each involves a 2D-convolution layer using ReLU followed by a max-pooling layer; 33 kernel; The three convolution layers use 32, 64, and 64 kernels, respectively.
  - A flatten layer.
  - A fully connected layer with 64 units.
  - An output layer using the Softmax function.

## Slide 18: Authentication Decision
Continual learning processor
- Basic idea: Protect the performance of the existing CNN-based model while modifying the elastic weight consolidation (EWC) method to adapt the CNN-based model to new training datasets.
- Unsupervised training dataset labeling:
  - Compare the probability that the current sample is from a valid user with a threshold , if , pseudo-label the sample as positive; otherwise pseudo-label the sample as negative.
  - Construct a new training dataset by selecting the top-70% positive/negative samples with the highest/lowest probabilities.

## Slide 19: Authentication Decision
Continual learning processor
- Basic idea: Protect the performance of the existing CNN-based model while modifying the elastic weight consolidation (EWC) method to adapt the CNN-based model to new training datasets
- Unsupervised training dataset labeling
- CNN model updating using EWC:
Surrogate loss
Traditional EWC loss
Modified loss function:

## Slide 20: Authentication Decision
Sampling controller
- Build a sampling function of interference intensity.

## Slide 21: Implementation
Data collection
- 45 participants (26 males and 19 females)
- Three months
- Each participant records 130-200 minutes
- Controlled lab room, home, and a park
- 24-hour evaluation
- Key algorithm evaluation
- Impact factor evaluation
- Long-term evaluation
Prototype
- ANC earphones with IEMs
- Sensing board

## Slide 22: Evaluation: Overall Performance
Replay attack:
  - Consider one participant as a valid user and the remaining participants as random attackers.
Average FAR 1.6%
Average FRR 1.8%

## Slide 23: Evaluation: Overall Performance
Replay attack:
  - Use medical records (i.e., chest PCG gathered via electronic stethoscopes) and a medical human silicone simulator to forge binaural bone-conducted PCGs.
Average FAR 2.3%

## Slide 24: Evaluation: Key Algorithms
Interference elimination:
  - Case i: IS=audio, IE=without
  - Case ii: IS=motion, IE=without
  - Case iii: IS=audio, IE=with
  - Case iv: IS=motion, IE=without
FAR and FRR below 2.5%
in 12 weeks
Continual learning:
  - Conduct experiment for 12 weeks.

## Slide 25: Evaluation：Practical Issues
Average FAR 2.0%
Average FRR 3.8%
24-hour study:
  - Conduct experiment for 24 hours (contains daily activities)
Earphone wearing states:
 | 0° | 45° | 90°
2mm | FAR=1.9% FRR=2.2% | FAR=2.1% FRR=2.5% | FAR=2.0% FRR=2.2%
4mm | FAR=1.6% FRR=1.9% | FAR=1.6% FRR=1.9% | FAR=1.6% FRR=1.9%
6mm | FAR=1.4% FRR=1.7% | FAR=1.4% FRR=1.8% | FAR=1.4% FRR=1.7%
8mm | FAR=1.4% FRR=1.6% | FAR=1.4% FRR=1.6% | FAR=1.4% FRR=1.6%
10mm | FAR=1.3% FRR=1.6% | FAR=1.4% FRR=1.6% | FAR=1.4% FRR=1.6%

## Slide 26: Conclusion
We propose a passive user authentication system, HeartPrint, using ANC earphones with IEMs.
HeartPrint exploits the unique binaural bone-conducted PCGs and IEMs.
We present several effective methods to achieve HeartPrint.
Interference elimination based on modified NMF.
Representation extraction, including heart motion feature, body conduction feature, and body asymmetry feature.
User authentication based on CNN-based framework and continue learning technology.
We design prototypes and conduct experiments with 45 participants.
HeartPrint is accurate and can resist various attacks.

## Slide 27
Thanks!
Thanks!
Thanks!
&
&
&
Questions
Questions
Questions
Yetong Cao
yetongcao@bit.edu.cn