## Slide 1
AWash: Handwashing Assistance for the Elderly with Dementia via Wearables
Presenter: Yetong Cao
Yetong Cao∗ Huijie Chen∗ Fan Li∗ Song Yang∗ Yu Wang†
*School of Computer Science and Technology, Beijing Institute of Technology, China †Department of Computer and Information Sciences, Temple University, USA

## Slide 2: Motivation
Memory Loss
？
？
Difficulty Completing Tasks

## Slide 3: Limitation of Existing Techniques
Vision-based Methods
Privacy
Wearable-based Methods
Different behavior patterns
More distinct individual differences in handwashing movement patterns
Diverse assistance manner
Ineffective

## Slide 4: Goals
1
Accurate
2
User-independent
3
Support diverse assistance manner
Wrist Posture
Handwashing Actions
Collect Data
Recognize
Assist
senile dementia patients

## Slide 5: Overview
C1:How to obtain each type of handwashing movement fragment from the continuous and noisy IMU sensor data?
C2:How to derive the repre-sentative wrist movement information to distinguish the various handwashing move-
ments of the elderly with dementia?
C3:How to design a user-independent handwashing motion recognition system for senile dementia patients with diverse cognitive impairment?

## Slide 6: Handwashing Actions Segmentation
1
Noise Reduction：
Moving average filter
？
？
？
Visuomotor impairment affects eye-hand coordination for the orderly in some dementias during handwashing
Interferences

## Slide 7: Handwashing Actions Segmentation
Data in window
Autocorrelation
Autocorrelation
2
Handwashing Action Detection：
Repetitive patterns！
Data in window
Autocorrelation
Data in window

## Slide 8: Handwashing Actions Segmentation
3
Start and End Position Detection：
Autocorrelation
Data in window
P

## Slide 9: Handwashing Information Derivation
1
Coordinate Transformation:
2
Sensor-Body Inclination Angles Calculation:
Device coordinate system
Earth coordinate system
Body coordinate system

## Slide 10: Action Recognition
We take prediction with the highest probability as the recognized action

## Slide 11: Handwashing Assisting
Type | Issue | Assistance Form
Mild dementia | Forget the handwashing process; Miss a few steps in the overall task | Practice handwashing actions in the same procedure
Moderate dementia | Forget how to perform a specific action; Have obsessive behaviors; Fail to focus on the task | Practice performing specific actions; Stop the wrong action
Severe dementia | More complex issues | 
1
Handwashing Process Modeling:
？
？
？
Uses tate machine to model hanwashing process.
2
Design of Audio Prompt:
Audio guidance：familiar with audio prompts, provides a more direct augmentation of executive function, do not distract users.
Gentle male voice, more straightforward commands, played loud enough.

## Slide 12: EVALUATION
Setup:
9-axis IMU sensor
100Hz
Ground truth:
camera
Recruitment:
8 participants
20 days
6,000 samples
ID | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Age | 81 | 75 | 74 | 71 | 71 | 68 | 65 | 65
Gender | F | M | M | F | M | M | F | M
MoCA | 21 | 20 | 18 | 21 | 25 | 27 | 23 | 28

## Slide 13: Performance of Handwashing Action Recognition
Recall: 92.94%
Precision: 92.60%
F1-score: 92.76%
delay < 0.9 s: 80.00%

## Slide 14: Issue Study
Long-Term Recognition Performance
Impact of Sink Height：
Recall, precision, and F1-score are all above 84%
Sink height | recall | precision | F1 score
Children Sink (25 in) | 81.74% | 83.50% | 82.10%
Mixed data | 87.86% | 88.61% | 88.07%

## Slide 15: Effectiveness of Handwashing Assistance
 | Prompt when miss steps in the overall task |  |  |  | Prompt when perform steps in wrong order |  |  | 
ID | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Baseline | 3.67 | 3.67 | 3.00 | 4.00 | 4.67 | 5.00 | 4.67 | 5.33
AWash 1st day | 5.40 | 5.40 | 5.40 | 5.60 | 5.80 | 6.00 | 5.80 | 6.00
Awash 20th day | 6.00 | 5.00 | 5.00 | 6.00 | 6.00 | 6.00 | 6.00 | 6.00

## Slide 16: User Experience
System Usability Scale (SUS) Questions:
I think that I would like to use this system frequently.
I find the system unnecessarily complex.
I think the system is easy to use.
I think that I would need the support of a technical person to be able to use this system.
I find the various functions in this system are well integrated.
I think there is too much inconsistency in this system.
I would imagine that most people would learn to use this system very quickly.
I find the system very cumbersome to use.
I feel very confident using the system.
I need to learn a lot of things before I could get going with this system.

## Slide 17: Conclusion
We present AWash, a cognitive assistive technology that takes a new step in helping the elderly with dementia washing their hands
  Only use commodity IMU sensor integrated on most wrist-worn devices (e.g., smartwatches) to collect handwashing data.
We propose a set of novel algorithms
  Autocorrelation-based handwashing movements segmentation method
  Quaternion-based coordinate transformation method
  A hybrid network model is achieve user-independent handwashing action recognition
  State machine-based user-define assistance.
We implement a prototype system and conduct experiments with 8 older participants
  Demonstrate the robustness and effectiveness of the system.

## Slide 18
Thanks!
Thanks!
Thanks!
&
&
&
Questions
Questions
Questions
Yetong Cao
yetongcao@bit.edu.cn