## Slide 1
Guard Your Heart Silently: Continuous Electrocardiogram Waveform Monitoring with Wrist-Worn Motion Sensor
Yetong Cao∗ Fan Li∗ Huijie Chen† Xiaochen Liu∗ Li Zhang‡ Yu Wang§
*School of Computer Science, Beijing Institute of Technology, China
† School of Computer Science, Beijing University of Technology, China
‡ School of Mathematics, Hefei University of Technology, China
§Department of Computer and Information Sciences, Temple University, USA
UbiComp 2022

## Slide 2: Background
Emotion Recognition
Biometric Identification
Physiological Metrics Monitoring
Electrocardiogram (ECG) measures the electrical activity of the heart, which has a unique waveform shape associated with cardiac cycles

## Slide 3: Current ECG Monitoring Solutions
Clinical Monitors
Household Monitors
Inconvenient

## Slide 4: Current ECG Monitoring Solutions
Wearable approaches
Expensive
Discontinuous

## Slide 5: Our Solution
We propose VibCardiogram
Low-Cost
Reliable
Continuous
Convenient
Unobtrusive
Wrist-worn devices
VibCardiogram
Motion Sensor

## Slide 6: Observation: Cardiogenic Body Vibrations

## Slide 7: VibCardiogram : Overview & Challenges
Challenge 1：
How to disentangle the wrist vibration induced by cardiac activities from noisy sensor data collected at the wrist?
Challenge 2：
How to segment each heartbeat in the complex cardiogenic body vibrations?
Challenge 3：
How to achieve accurate and fine-grained ECG waveform shape estimation

## Slide 8: VibCardiogram : Wrist Vibration Extraction
Signal Preprocessing
  Bandpass filtering (4th-order Butterworth, [5 Hz-30 Hz])
  Linear interpolation
Movement Noise Cancellation
Stable
Periodic
Noisy
Non-periodic

## Slide 9: VibCardiogram : Wrist Vibration Extraction
Signal Preprocessing
  Bandpass filtering (4th-order Butterworth, [5 Hz-30 Hz])
  Linear interpolation
Movement Noise Cancellation
  Stationary Wavelet Transform (SWT)-based noise reference generation
Interference
reference

## Slide 10: VibCardiogram : Wrist Vibration Extraction
Signal Preprocessing
  Bandpass filtering (4th-order Butterworth, [5 Hz-30 Hz])
  Linear interpolation
Movement Noise Cancellation
  Stationary Wavelet Transform (SWT)-based noise reference generation
  Adaptive filter-based noise cancellation
Cardiogenic body vibrations

## Slide 11: VibCardiogram : Vibration Signal Segmentation
Spike Point Identification
R peak

## Slide 12: VibCardiogram : Vibration Signal Segmentation
Spike Point Identification
  Detect all local maximum/minimum points in the vibration signal

## Slide 13: VibCardiogram : Vibration Signal Segmentation
Spike Point Identification
  Constructed triangles based on local maximum (peak) and its two adjacent local minimums (trough)

## Slide 14: VibCardiogram : Vibration Signal Segmentation
Spike Point Identification
  Extract geometric features in each triangle

## Slide 15: VibCardiogram : Vibration Signal Segmentation
Spike Point Identification
  Compare feature correlations and select to input into the random forest to identify spike points
Feature | Spike points |  |  | Other points |  | 
 | AVG | MED | STD | AVG | MED | STD
a+b | 1.221 | 1.165 | 0.384 | 0.427 | 0.349 | 0.104
c | 0.160 | 0.150 | 0.004 | 0.093 | 0.08 | 0.004
d | 0.470 | 0.433 | 0.009 | 0.221 | 0.150 | 0.046
e | 0.738 | 0.803 | 0.238 | 0.189 | 0.094 | 0.061
f | 0.385 | 0.324 | 0.043 | 0.848 | 0.698 | 0.295
g | 0.971 | 0.491 | 0.954 | 1.253 | 1.364 | 0.815
h | 1.355 | 0.840 | 1.064 | 1.041 | 0.574 | 0.985

## Slide 16: VibCardiogram : Vibration Signal Segmentation
Heartbeat Fragment Extraction
  Identify the 250 ms before the spike point as the boundary of a heart cycle
250 ms
250 ms
250 ms

## Slide 17: VibCardiogram : ECG Estimation
Encoder-Decoder Model Building

## Slide 18: VibCardiogram : ECG Estimation
Encoder-Decoder Model Boosting
Loss of generator:
Loss of discriminator:

## Slide 19: Evaluation
Setup
  IMU prototype
Data Collection
  20 participants (10 male,10 female)
  Various body movements, sampling rates, sensor positions
Ground Truth
  AD8232-based device
Metrics
  Estimation Error:
  Correlation Coefficient:
IMU
Adjustable wrist band

## Slide 20: Evaluation: Overall Performance
75% data for training and the rest 25% data for testing
Estimation Error:
Average 5.989% 2.496%
Correlation Coefficient:
Average 0.926 0.030

## Slide 21: Evaluation: Emotion Recognition
Comparison of our method with typical methods in emotion recognition
Stimuli emotions using video clips
Estimate ECG waveform
Extract HRV features
Classify emotion using SVM

## Slide 22: Conclusion
We propose the first IMU-based wearable ECG waveform estimation system that achieves low-cost, continuous, reliable, convenient, and unobtrusive
We design a set of techniques to ensure accurate ECG estimation
Evaluation Results are promising
More details？
Yetong Cao, Fan Li, Huijie Chen, Xiaochen Liu, Li Zhang, Yu Wang,
Guard Your Heart Silently: Continuous Electrocardiogram Waveform Monitoring with Wrist-Worn Motion Sensor,

## Slide 23
Thanks!
Thanks!
Thanks!
&
&
&
Questions
Questions
Questions
Yetong Cao
yetongcao@bit.edu.cn